Biosonics training Wed 4/16/08 10am  Eric, Brian

USB Hard drive

Compatible GPS?

Installation:

Software

Biosonics (and Echoview?)

Hardware

Transducer

Cone angle?  (Table of ensonified area?)

200 kHz = 0.75cm

Max range?  (Parts of Haro are >200m)

GPS

Expected port (input)

External hard drive

Write direct, or intermittent xfers?

Mounting

Swivel mount

Pole dimensions and material (Al? inner/outer dia?)

Acquisition

Noise

Engine noise?

Electrical noise?

Noise reduction filter?

Time varied gain?

Survey design

Fixed grid: Transect on/off-shore at Lime Kiln (near lingcod tags)

Adaptive: When paralleling KWs, cross path before/after on same line?

Classification of Prey Assemblages

38 kHz (Horne and Gauthier, ’04) vs 200 kHz?

Split beam?  Dual-frequency?

Products and processing

Goals:

Fish abundance (biomass), size categories, and their distribution

Categories of returns?

Depth binned returns?

Backscatter categories (a la Horne+Gauthier)?

Target strength bins?

Model of L~f(TS)?

Bottom depth (georeferenced)

Bottom type categorization

Software

Visual Analyzer 4.1

(vs Echoview)

EcoSav?

Biomass vs Sa?

Integration threshold (-75dB)

Elementary distance sampling unit (EDSU) or horiz bin size

Max vertical integration depth

Fish densities in the water column are reported as Area Backscattering Coefficients (i.e. sa, units m2m-2). This nondimensional quantity is the integral of the volume backscattering coefficient (sv) over a range interval z1 to z2:

The volume backscattering coefficient is the total energy of all targets (σbs) in a specified volume V (i.e. sv = Σσbs/V).

Categories of returns?

Backscatter categories (a la Horne+Gauthier)?

Depth binned

Target strength bins?

Model of L~f(TS)?

Bottom depth (georeferenced)

Bottom type categorization